## Slide 2: Storage Latency for Oracle DBAs
Luca Canali – CERN
Marcin Blaszczyk - CERN

## Slide 3: Outline
CERN and Oracle
Latency: what is the problem we are trying to solve
Storage latency in Oracle
Examples
Tools
Conclusions

## Slide 4: Outline
CERN and Oracle
Latency: what is the problem we are trying to solve
Storage latency in Oracle
Examples
Tools
Conclusions

## Slide 5: CERN
European Organization for Nuclear Research founded in 1954
20 Member States, 7 Observer States + UNESCO and UE
60 Non-member States collaborate with CERN
2400 staff members work at CERN as personnel, 10 000 more researchers from institutes world-wide

## Slide 6: LHC, Experiments, Physics
Large Hadron Collider (LHC)
  World’s largest and most powerful particle accelerator
  27km ring of superconducting magnets
  Currently undergoing upgrades, restart in 2015
The products of particle collisions are captured by complex detectors and analyzed by software in the experiments dedicated to LHC
Higgs boson discovered!
The Nobel Prize in Physics 2013 was awarded jointly to François Englert and Peter W. Higgs "for the theoretical discovery of a mechanism that contributes to our understanding of the origin of mass of subatomic particles, and which recently was confirmed through the discovery of the predicted fundamental particle, by the ATLAS and CMS experiments at CERN's Large Hadron Collider"
Notes: New particle discovery: see also CMS and Atlas announcement on July 4th 2012.

## Slide 7: WLCG
The world’s largest scientific computing grid
  More than 100 Petabytes of data stored and analysed. Increasing: 20+ Petabytes/year
  Over 68 000 physical CPUs
  Over 305 000 logical CPUs
  157 computer centres in 36 countries
  More than 8000 physicists with real-time access to LHC data

## Slide 8: CERN’s Databases
~100 Oracle databases, most of them RAC
  Mostly NAS storage plus some SAN with ASM
  ~500 TB of data files for production DBs in total
Examples of critical production DBs:
  LHC logging database ~170 TB, expected growth up to ~70 TB / year
  13 Production experiments’ databases
Relational DBs play a key role in the LHC production chains
  Accelerator logging and monitoring systems
  Online acquisition, offline: data (re)processing, data distribution, analysis
  Grid infrastructure and operation services
    Monitoring, dashboards, etc.
  Data management services
    File catalogues, file transfers, etc.
  Metadata and transaction processing for tape storage system

## Slide 10: Outline
CERN and Oracle
Latency: what is the problem we are trying to solve
Storage latency data in Oracle
Examples
Tools
Conclusions

## Slide 11: Latency
Latency, a measure of time.
  In the context of this presentation: time to access data

## Slide 12: Understanding Latency
How long I should wait for baby elephant?
  Elephant gestation period ~22 month
  Latency: 22 months

## Slide 13: Understanding Throughput
What if I want 2 baby elephants?
Throughput has doubled:
  2 elephants in 22 months
Latency: still 22 months

## Slide 14: I/O Operations Per Second
IOPS is a measure of throughput
IOPS depends also on latency
Latency differs for
  ‘random’ reads
  ‘sequential’ reads
How can we get more IOPS without increasing the latency?
  Use Many HDDs!

## Slide 15: Why We Care About Storage Latency
Performance analysis and tuning:
  Where is the time spent during a DB call?
  What response time do the users see from the DB?
OLTP-like workloads:
  Response time can be dominated by I/O latency
  Index-based access, nested loops joins

## Slide 16: Physical Sources of Latency
Blocking I/O calls:
  Think access to a large table via an index
  Random access
  HDD: head movement and disk spinning latency

## Slide 17: What can we do: Hardware
Current trends for HW
  Large SSD cache in storage
  Tiered storage
  Servers with large amounts of memory
    Reduce (random) reads
    Caching large amounts of data
    Trends towards in-memory DBs
A balance act performance vs. cost

## Slide 18: What can we do: Software
Big gains in application/SQL optimization
  SW optimisation beats HW optimisation most of the times
Oracle tuning:
  Understand when single-block access is not optimal
  Full scan vs. index-based access
  Hash join vs. nested loop
  In general: get a good execution plan

## Slide 19: So Where is the Problem?
DB Admin:
- Storage is slow!
Storage Admin:
- The problem is with the DB!
Reality check:
  Lack of clear storage performance data.
  Changing database workloads.

## Slide 20: Outline
CERN and Oracle
Latency: what is the problem we are trying to solve
Storage latency in Oracle
Examples
Tools
Conclusions

## Slide 21: Transactional Workload
Example from OEM
  DB time dominated by ‘db file sequential read’
    CPU is not a bottleneck
    Ignore locks and other serialization events

## Slide 22: Oracle Wait Events
Can we troubleshoot a storage issue from the DB engine?
  Not in the general case
What can we do?
  Oracle wait event instrumentation is great
  Wait event histograms is a key source of data

## Slide 23: Wait Event Analysis
We want to drill down
  ‘db file sequential read’ wait event
  Also useful for ‘log file sync’ event
What can we gain?
  Make educated guesses of what is happening on the storage
  Attack the root causes of the problem

## Slide 24: A Story From Our Production
Migrated to a new storage system
  NAS storage with SSD cache
  Good performance: because of low-latency reads from SSD
Issue:
  From time to time production shows unacceptable performance
Analysis:
  The issue appears when the backup runs!

## Slide 25: Wait Event Drill Down
Very slow reads appear
Reads from SSD cache go to zero
Number of waits
Notes: Data taken from AWR and in particular wait event histograms data aggregating over RAC nodes.
Example:
select cast(sn.begin_interval_time as date) snap_time,
--eh.dbid,
sn.instance_number,
eh.event_name,
eh.wait_time_milli,
--eh.wait_count,
eh.wait_count - lag(eh.wait_count) over (partition by eh.dbid,eh.instance_number,eh.event_id,eh.wait_time_milli order by sn.snap_id nulls first) Delta_wait_count,
round((eh.wait_count - lag(eh.wait_count) over (partition by eh.dbid,eh.instance_number,eh.event_id,eh.wait_time_milli order by sn.snap_id nulls first)) /
(extract(hour from END_INTERVAL_TIME-begin_interval_time)*3600
-extract(hour from sn.snap_timezone - lag(sn.snap_timezone) over (partition by eh.dbid,eh.instance_number,eh.event_id,eh.wait_time_milli order by sn.snap_id nulls first) )*3600 --deals with daylight savings time change
+ extract(minute from END_INTERVAL_TIME-begin_interval_time)* 60
+ extract(second from END_INTERVAL_TIME-begin_interval_time)),2 ) Rate_wait_count_per_bin
from dba_hist_event_histogram eh,
dba_hist_snapshot sn
where
sn.snap_id = eh.snap_id
and sn.dbid = eh.dbid
and sn.instance_number = eh.instance_number
and sn.begin_interval_time &delta_time_where_clause
and eh.wait_class in ('User I/O','System I/O','Commit') -- need to limit search or dump file can grow too big
order by sn.snap_id;

## Slide 26: What We Found
AWR data used to examine the issue
  DBA_HIST_EVENT_HISTOGRAM
  Wait event: db file sequential read
I/O slow during backups
  because fewer I/O requests were served from SSD
Note: how we worked around this issue
  Short term: moved backup to Active Data Guard replica
  Medium term: upgraded filer model

## Slide 27: Lesson Learned
If response time is dominated by db_file_sequential_read
  Drill down on wait event histogram
  Average latency values are not good enough
  Latency details provide info on what is happening on the storage

## Slide 28: Real-Time Monitoring
Problem:
  How to perform real-time monitoring of the event latency?
Answer: V$EVENT_HISTOGRAM
  Cumulative counters
  We need to compute deltas

## Slide 29: Monitoring Latency - Snapshots
Custom script: ehm.sql
Script can be downloaded from: http://canali.web.cern.ch/canali/resources.htm

## Slide 30: Monitoring Latency - Snapshots

## Slide 31: Display Latency Data over Time
It’s a three dimensional representation:
  Latency bucket, value, time
This problem has been solved before!
Heat Map representation
  Used for example in Sun ZFS Storage 7000 Analytics
  Reference: Brendan Gregg, Visualizing system latency, Communications of the ACM, July 2010

## Slide 32: Heat Maps
By Definition
  graphical representation of data where the individual values contained in a matrix are represented as colours (wikipedia)
Examples:

## Slide 33: Latency Heat Maps - Frequency
X=time, Y=latency bucket
Colour=events per second (e.g. IOPS)

## Slide 34: Latency Heat Maps - Frequency
X=time, Y=latency bucket
Colour=events per second (e.g. IOPS)
TIME

## Slide 35: Latency Heat Maps - Frequency
X=time, Y=latency bucket
Colour=events per second (e.g. IOPS)

## Slide 36: Latency Heat Maps - Frequency
X=time, Y=latency bucket
Colour=events per second (e.g. IOPS)

## Slide 37: Latency Heat Maps - Frequency
X=time, Y=latency bucket
Colour=events per second (e.g. IOPS)

## Slide 38: Another Metric of Interest
How much time do we wait in a given bucket?
  Not directly available in v$event_histogram
How to estimate it? Example:
  100 waits in the bucket 8ms means
  Wait time between 100*4 ms and 100*8 ms
  Approximate: 100 * 6 ms [that is 100 * ¾ * 8 ms]
Definition:
  Intensity = 0.75 * bucket_value * frequency_count

## Slide 39: Latency Heat Maps - Intensity
X=time, Y=latency bucket
Colour= intesity [time waited per bucket]

## Slide 40: Outline
CERN and Oracle
Latency: what is the problem we are trying to solve
Storage latency in Oracle
Examples
Tools
Conclusions

## Slide 41: Stress Testing
Scenarios
  Investigate HW performance
  Compare different systems
  Example: compare current storage with a new system
It’s hard:
  Choose test workloads that make sense
  Understand effects of caching

## Slide 42: SLOB 2
An Oracle-based stress testing tool
  Search: “SLOB 2 by Kevin Closson”
Great tool generate lots of random IO
  Directly from Oracle processes
  Physical reads from storage
    Become Oracle’s wait events for db file sequential read
Size of test data is configurable
Concurrency is configurable

## Slide 43: Example: “Too Good To Be True”
Lesson learned: test data size was too small
23 SAS disks delivering 20K IOPS?
It doesn’t make sense
Latency is the clue
Reads served by controller cache!

## Slide 45: Example: “Too Good To Be True”
Lesson learned: test data size was too small
23 SAS disks delivering 20K IOPS?
It doesn’t make sense
Latency is the clue
Reads served by controller cache!

## Slide 46: Example: “Load Till Saturation”
Lesson learned: don’t accept IOPS numbers without latency values
23 SAS disks
JBOD & ASM
4 consecutive
tests with
increasing load

## Slide 47: Example: “Load Till Saturation”
Lesson learned: don’t accept IOPS numbers without latency values
23 SAS disks
JBOD & ASM
4 consecutive
tests with
increasing load

## Slide 48: Example: “Load Till Saturation”
Lesson learned: don’t accept IOPS numbers without latency values
23 SAS disks
JBOD & ASM
4 consecutive
tests with
increasing load

## Slide 49: IOPS and Latency are Related
Observation: as IOPS approach saturation latency increases fast
Confirmed: a simple model from queueing theory:
Calculation performed using
MMm Multiserver model
By Cary Millsap, 2003
Chart: Response Time = Service Time + Queueing Delay
| 0 | 225 | 450 | 675 | 900 | 1125 | 1350 | 1575 | 1800 | 2025 | 2250 | 2475 | 2700 | 2925 | 3150 | 3375 | 3600 | 3825 | 4050 | 4275 | 4500
R for graphical display | 5 | 5.2571 | 5.5422 | 5.8599 | 6.2162 | 6.6187 | 7.0769 | 7.6033 | 8.2143 | 8.932 | 9.7872 | 10.8235 | 12.1053 | 13.7313 | 15.8621 | 18.7755 | 23 | 29.6774 | 41.8182 | 70.7692 | 230
R for graphical display | 0.005 | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A | #N/A

## Slide 50
0.5 TB dataset, 100% in SSD, 56 sessions, random reads - NAS system

## Slide 51
10TB dataset, 128 sessions, random reads, disk saturation - NAS system

## Slide 52: Monitoring Production Systems
Understand I/O response time
  Help for tuning and capacity planning
  Attack questions like: is the storage slow?
Drill down on three areas:
  I/O served by SSD/controller cache
  I/O served by physical disk ‘spindles’
  I/O with very large latency: outliers

## Slide 53: An Example of a Busy System

## Slide 54: What Can We Learn?
Example of analysis
  i.e. drill down ‘db file sequential read’
Are disks close to saturation?
  NO, but latency high (SATA disks)
I/O outliers?
  YES, Further investigation on controller needed
Do we have SSD/cache?
  YES, ~30% reads with low latency
  We could profit from a larger SSD cache maybe?

## Slide 55: Log File Sync
Example from a production system
Low latency from
writes because of
storage cache

## Slide 56: Log File Sync
Example from a production system
low latency from
writes because of
storage cache

## Slide 57: Log File Sync
Example from a production system
Low latency from
writes because of
storage cache

## Slide 58: Log File Sync
Anomaly, on a test system
High latency
caused by HW
Issues and high
load from Oracle

## Slide 59: Log File Sync
Anomaly, on a test system
High latency
caused by HW
Issues and high
load from Oracle

## Slide 60: Log File Sync
Anomaly, on a test system
High latency
caused by HW
Issues and high
load from Oracle

## Slide 61: Limitations
Wait event timing is done by Oracle code
  May not reflect actual I/O service time
  CPU time may also be accounted as I/O wait
  Server high load can distort the timing values
  V$event_histogram has only milli sec precision
Asynchronous I/O
  Wait events of this family are very hard or impossible to utilize in the context of latency
Notes:     Asynch IO, for example in Linux for block devices: OS calls (ASM example): io_submit(), io_getevents
We can tap Oracle code with DTrace to see where the wait event timing is handled:
# this is for Oracle 11.2.0.3, Linux and Solaris: trace os process pid=1737 (edit os pid as relevant) dtrace -n ' pid1737:oracle:kews_update_wait_time:entry {
self->ela_time = arg1;
}
pid1737:oracle:kskthewt:entry {
printf("event#= %d, time(mu sec) = %d", arg1, self->ela_time);
}'

## Slide 62: Blocking Calls
Db file sequential read
  Is the easiest event to relate to I/O service time
  Instruments single-block reads, blocking I/O
    Note: in some cases Oracle can use async I/O for random reads, e.g. for prefetching and batching. Wait event used in that case is ‘db file parallel read’
Log file sync
  Big part of the commit-time wait
  Complex: it’s not a pure I/O event
  The root causes of high latency here can also be CPU starvation and LGWR behaviour (e.g. bugs)
Notes: Log file sync: From 11.2.0.3 adaptive mechanism
Automatic switching to a poll-based method instead of post-based
Disable this behaviour with: alter system set “_use_adaptive_log_file_sync”='FALSE‘;
Disable Oracle optimizations such as prefetching when testing random reads. See SLOB documentation and parameters:
_db_block_prefetch_limit=0
_db_block_prefetch_quota=0
_db_file_noncontig_mblock_read_count=0

## Slide 63: Latency and Trace Files
Latency data is available in 10046 trace files
  With micro second precision
  Allows drill down to session level
    As opposed to using global GV$ views
nam='db file sequential read' ela= 977 file#=7 block#=29618220 blocks=1 obj#=82015 tim=1377520823036634
SQL> exec dbms_monitor.session_trace_enable(sid,serial#)

## Slide 64: More Latency Sources
DTrace
  Great performance tool, coming to Linux too
  Can be used to gather I/O latency histograms
    Use of the quantize operator
dtrace -n '
syscall::pread64:entry { self->s = timestamp; }
syscall::pread64:return /self->s/ { @pread["ns"] = quantize(timestamp -self->s); self->s = 0; }
tick-10s {
printa(@pread);
trunc(@pread);
}'

## Slide 65: Outline
CERN and Oracle
Latency: what is the problem we are trying to solve
Storage latency in Oracle
Examples
Tools
Conclusions

## Slide 66: Tools
Automate tedious tasks
  Data collection
  Visualisation
Provide data and help answer questions
  Drill down on I/O wait events
Find trends and evolution
  How does performance change over time
  Is it Oracle workload changing or is it the storage that has become slow?

## Slide 67: Tools: PerfSheet 4
Simple Analytic platform for AWR data
Predefined queries and graphs
Power of Pivot Charts

## Slide 68: Tools: PerfSheet 4
Simple Analytic platform for AWR data
Predefined queries and graphs
Power of Pivot Charts

## Slide 69: Tools: PerfSheet 4
Simple Analytic platform for AWR data
Predefined queries and graphs
Power of Pivot Charts

## Slide 70: Tools: OraLatencyMap
It’s a SQL*Plus script based on PL/SQL
  Lightweight, does not require any installation
  Command line interface
  Heat Maps generated using ANSI escape codes
Get started:
SQL> @OraLatencyMap

## Slide 71: Tools: PyLatencyMap
It’s written in Python + SQL*Plus scripts
  No installations required, CLI, lightweight
  More advanced than OraLatencyMap
Can be used for generic latency sources
    Oracle v$, trace files, AWR, DTrace data, etc
    Pre-built examples available
Feature: record and replay

## Slide 72: Getting Started with PyLatencyMap
Modular architecture
  Source | <optional filter> | visualization engine
Get started
Video, getting started with PyLatencyMap
http://www.youtube.com/watch?v=-YuShn6ro1g
./Example1_oracle_random_read.sh

## Slide 73: Outline
CERN and Oracle
Latency: what is the problem we are trying to solve
Storage latency in Oracle
Examples
Tools
Conclusions

## Slide 74: Conclusions
Analysis of I/O latency
  A powerful technique in performance tuning
  Latency average is not enough, need histograms
  Oracle wait interface has histogram details
PylatencyMap for data collection and visualisation
  for Oracle and generic data sources
  http://cern.ch/canali/resources.htm
Latency heat maps are great!

## Slide 75: Acknowledgements
Our colleagues in the CERN Database Group
  In particular: Ruben Gaspar
Many ideas borrowed from blogs and articles:
  Brendan Gregg, Tanel Poder, Kevin Closson, Frits Hoogland, Marcin Przepiorowski, James Morles, Kyle Hailey, Cary Millsap

## Slide 76
Thank you!
Luca.Canali@cern.ch
Marcin.Blaszczyk@cern.ch