## Slide 1
CERN openlab Open Day
10 June 2015
KL Yong
Sergio Ruocco
Data Center Technologies Division
Speeding-up Large-Scale Storage with Non-Volatile Memory

## Slide 2
Founded in 1992, DSI’ vision is to be a vital node in a global community of knowledge generation and innovation, nurturing research talents and capabilities for world class R&D in next generation technologies.
To establish Singapore as an R&D center of excellence in data storage technologies.
about
DSI
mission
vision

## Slide 3
10Tb/in2 areal density technologies
Thin Hybrid HDD (0.5TB 2.5”, 5mm, hybrid HDD)
STT-MRAM
ReRAM
Signal Processing & Error Correction
IC Design
Nanofabrication
Spintronics
Plasmonics
Photo-Electronics
Metamaterials and Small Particle Physics Research
NVM System
Active Hybrid Storage System
Big Data Analytics Platform
Data & Storage Security
NON-VOLATILE
MEMORIES
HARD DISK DRIVE
TECHNOLOGIES
DATA CENTER TECHNOLOGIES
ADVANCED CONCEPT & NANOFABRICATION TECHNOLOGIES
Core Competencies
Notes: Top to bottom

## Slide 4: Massive Data Key Challenge for Data Center
CAPEX cost for additional IT equipment - servers, networks and storage
Driving the energy costs
Larger footprint and space required
Increasingly challenging and costly to scale and deliver performance
Increasing complexity in operating and managing the data center
Providing data protection and security for massive amount of data
Performance
Scalability
Energy Consumption
Manageability
Space
Security

## Slide 5
Integration of
Active Drive
Hybrid Drive
NVM
Hard Disk
Controller
NVM
Cache
Magnetic
Media
Open
Flow
Software
Managed
Homomorphic
Security
Future Data Center Architecture with Emerging Technologies
Performance, scalable, secured, energy and cost efficient
Notes: A total of $13.8M SGD allocated for 7 projects over 3 years,

## Slide 6
Next Generation Non Volatile Memory (NVM)
Characteristics of next generation NVM:
+ high speed ~ DRAM like
+ data persistent against power loss
+ byte-addressable (vs 4KB- 512KB blocks)
+ endurance (~DRAM like) >>> Flash
+ no refresh cycles/energy
Technology | Read | Write | Endurance Cycle | Read (V) | Write (V) | Maturity
HDD (15KRPM) | 6000μs | 6000μs | NA | 5V, 12V | 5V,12V | Product
SLC Flash | 25μs | 200μs/1.5ms (Program/Erase) | 105 (1000x for MLC) | 2 | 15 | Product
DRAM | <10ns | <10ns | 1016 | 1.8 | 2.5 | Product
STT-MRAM | 2-20ns | 2-20ns | 1015 | 0.7 | + 1 | Advanced Development

## Slide 7: NVM Research in DSI: Device to System
NVM Device
NVM Controller
NVM-based Systems
I/O Flow, Scheduling, Buffering
Wear Leveling
Erasure Coding
FPGA and firmware
NVM File System
System, Memory & Storage Stacks
Programming Model, Language & Toolchains
NVM Systems
Cluster
Materials & Structure
Signal Processing
Process
IC Integration

## Slide 8
Next Generation Non-Volatile Memory
2usec
50usec
8msec
8000
To fully exploit its performance, the hardware architecture and OS stacks including programming model – applications, languages, compilers/VMs, run-time libraries, middleware,... – must change

## Slide 9
Application
Application
Direct memory
load/store
NVM Programming Primitives & Lib
POSIX
File System
NVM
NVM Software Programming Model
  New programming model for NVM provides data persistence integrated into the application programs:
Byte-addressable
Load/Storage access without demand paging
Memory performance
Notes: Programming model and primitives for persistent NVM
NVM software compiler and toolchains
NVM runtime libraries
OS support

## Slide 10: CERN EOS NameSpace
9.6M files
68M files
93M files
4.4M files
7.4M files
100GB+ RAM
EOS node
catalog or NameSpace
client 1
client 2
client 100
client 1000+
disk-based log
50+ PB experimental data in 150M+ files across 5 experiments (nodes): ATLAS, CMS, LHCB, ALICE… Node availability critical for the continued operation of thousands of clients
Metadata operations (create, rename, move, delete etc.) are sped-up by in-memory NameSpace, with a growing RAM footprint of 100+ GBs Disk-based logs enable consistent reconstruction of NameSpace to recover after any hw & sw faults

## Slide 11: Challenges: Availability and Consistency
One of the challenges is the consistent journaling of metadata updates between memory and disk logs; but also across failures of the NS service, the hardware or power.
Reconstructing a 100GB+ Catalog can take even 10 minutes, disrupting client’s work.
Reconstruction is not IO-bound but CPU-bound because data structures trade-off lookup speed against insert speed.
Read-only FailOver
client 1
client 2
client 100
client 1000+
disk-based log
Failed & recovering

## Slide 12: Proposed Solution: EOS Catalog in Non-Volatile Memory
Store the instance of the EOS Catalog in Non-Volatile Memory. NVM-based Catalog is persistent, fault-tolerant, and always consistent. No more slow reconstructions from logs
.
Volatile memory
Read-Write Node
client 1
client 2
client 100
client 1000+
disk-based log
Failed & recovering
Non-Volatile Memory
Persistent Catalog

## Slide 13
of Enabling
Storage
Technologies